## Slide 1: src/main/scala Digital design with Chisel and friends
Tayyeb Mahmood (Phd, KAIST 2013)

## Slide 2: About Me
Postdoc researcher in Incheon National university, working in MLCAD, ML Architectures 2021-present
Assistant Professor (RCET-UET) 2013-2021
Research Interests:
  Embedded systems/IoT
  ML/Edge architectures
  EDA/MLCAD

## Slide 3: 1. Introduction to Chisel

## Slide 4: 1.1 What is Chisel?
Chisel is a hardware description language (HDL) that allows for high-level hardware design, enabling engineers to write code that describes the desired functionality of a digital circuit.
Unlike conventional HDLs like VHDL or Verilog, Chisel is embedded within a host programming language, typically Scala. This gives designers the power of a general-purpose programming language to express complex hardware designs efficiently, with increased productivity and readability.
One key characteristic of Chisel and friends is their support for hardware generators. These generators enable the automatic generation of hardware circuits based on input parameters, reducing the need for manual coding and improving the design's scalability.

## Slide 5: 1.2 Chisel vs Verilog
Verilog
module Adder (
  input wire [3:0] a,
  input wire [3:0] b,
  output wire [3:0] sum
);
  assign sum = a + b;
endmodule
Chisel3
import chisel3._
class Adder extends Module {
  val io = IO(new Bundle {
    val a = Input(UInt(4.W))
    val b = Input(UInt(4.W))
    val sum = Output(UInt(4.W))
  })
  io.sum := io.a + io.b
}

## Slide 6: 2. Basics of Digital Design with Chisel

## Slide 7: 2.1 Constructs
Chisel uses a hierarchical module-based design approach, similar to Verilog.
You can define modules and their connections using Chisel constructs like Input, Output, Module, Wire, and Reg.
Chisel supports both combinational and sequential circuit designs. Combinational circuits are created using combinational logic operators, while sequential circuits are created using registers and sequential constructs.

## Slide 8: 2.2 Combinational Design
Combinational circuits in Chisel are constructed using combinational logic operators such as && (AND), || (OR), ! (NOT), and ^ (XOR). These operators allow you to define logical relationships between input and output signals.
Chisel provides built-in types like Bool, UInt and SInt. These types can be used to define input and output ports of combinational modules.
Chisel use the := operator to assign the output to a signal.
Chisel allows the use of conditional expressions, such as Mux, to implement multiplexers (MUX) in combinational circuits.

## Slide 9: 2.3 Sequential Design
The Reg construct in Chisel3 is used to declare registers. It takes the data type as a parameter and returns a register of that type. For example: val myReg = Reg(UInt(8.W))
The RegInit construct initializes a register with a specific value. It takes the initial value as a parameter and returns a register initialized with that value. For example: val myReg = RegInit(0.U(8.W))
The RegEnable construct in Chisel3 is used to create a register with an enable signal. It takes the data type, initial value, and enable signal as parameters and returns a register with the specified properties. For example: val myReg = RegEnable(0.U(8.W), enableSignal)
Combinational logic is used to compute the next state based on the current state and input, while registers store the current state.

## Slide 10: 3. Chisel Fundamentals

## Slide 11: 3.1 Vectors
Vectors allow for the creation of arrays of elements with a fixed size and common data type.
Vectors are useful for representing multi-bit signals or collections of data that have a regular structure.
They can be used to create registers, memories, or other data structures that require storing multiple elements.
Vectors can be indexed and sliced to access individual elements or subranges of elements.
They provide a convenient way to perform parallel operations on multiple elements simultaneously.
Vectors can be used to represent input and output ports of modules, allowing for easy connectivity between different components.
They are commonly used in digital design for implementing shift registers, counters, FIFOs, and other sequential circuits.
Vectors can be used to create parameterized designs, where the size of the vector is determined at runtime or based on external parameters.
They provide a concise and efficient way to describe repetitive or patterned structures in a design.
Vectors can be used in combination with other Chisel constructs, such as bundles and modules, to create complex hierarchical designs.

## Slide 12: 3.2 Bundles
Bundles allow for the creation of composite data types that can group together multiple signals or elements with different data types.
Bundles are useful for representing structured data or complex interfaces that require multiple signals to be grouped together.
They provide a way to organize and encapsulate related signals, improving code readability and maintainability.
Bundles can be nested, allowing for the creation of hierarchical data structures and complex designs.
They can be used to represent the input and output ports of modules, facilitating easy connectivity between different components.
Bundles allow for the creation of custom data types that can have fields with different data types (e.g., UInt, Bool, Vec, or even other Bundles).
They enable the creation of parameterized designs, where the field types and sizes can be determined at runtime or based on external parameters.
Bundles provide a convenient way to perform hierarchical connects, allowing for easy connection of signals between different modules or submodules.
They can be used to create reusable components that encapsulate a set of related signals, improving modularity and code reuse.
Bundles can be used in combination with other Chisel constructs, such as vectors and registers, to create complex and structured designs.

## Slide 13: 3.3 I/O ports
Chisel I/O ports are used to define the input and output interfaces of Chisel modules.
Ports can be declared as input (Input()) or output (Output()) to specify the direction of data flow.
They provide a standardized way to define the communication between different modules or components.
Ports can be of various data types, including UInt, Bool, Vec, and Bundles.
They allow for the easy connection of signals between different modules, ensuring proper connectivity and data exchange.
Ports can be used to define the external interface of a module, enabling communication with the outside world.
They can be connected to other ports within a module or connected to external pins when generating Verilog or other target hardware descriptions.
Ports can have names, making it easier to reference and connect them to other signals or modules.
They enable the creation of parameterized designs, where the size and type of the ports can be determined at runtime or based on external parameters.
Chisel I/O ports provide a way to encapsulate and organize the inputs and outputs of a module, improving code readability and maintainability.
They support bidirectional communication by allowing the declaration of Flipped ports, which reverse the direction of data flow.

## Slide 14: 3.4 Modules
Chisel modules are the building blocks of digital designs in Chisel and represent hardware components or modules.
Modules in Chisel are defined using classes that extend from the RawModule, BaseModule, or Module classes.
RawModule is the base class for all modules in Chisel. It provides a basic structure for modules and includes methods for adding signals and submodules.
BaseModule extends RawModule and adds features such as default clock and reset signals, as well as methods for defining module-level parameters and generating Verilog code.
Module is a subclass of BaseModule and provides additional features such as automatic generation of I/O ports and support for hierarchical module construction.
Module is the recommended class to use for defining Chisel modules, as it provides a higher-level interface and simplifies the module construction process.
Modules can have input and output ports, which are defined using Chisel I/O ports. These ports define the communication interfaces of the module with the outside world.
Modules can contain signals, registers, combinational logic, and submodules, allowing for the creation of complex and hierarchical designs.
Modules can be instantiated and connected together to build larger systems, forming a hierarchical structure.
Modules can be parameterized, allowing for the creation of reusable and configurable designs. Parameters can be used to control the size, behavior, or configuration of the module.

## Slide 15: 3.5 Clock and Reset domains
Clock Domain: A clock domain represents a specific clock signal that controls the timing of operations within a module. In Chisel, the clock domain is typically associated with a Clock signal.
Reset Domain: A reset domain represents a specific reset signal that initializes or resets the state of a module. In Chisel, the reset domain is typically associated with a Reset signal.
Synchronous Logic: Synchronous logic refers to the design elements that are synchronized with a clock signal. This includes registers, counters, and other sequential elements.
Asynchronous Logic: Asynchronous logic refers to the design elements that are not directly synchronized with a clock signal. These elements typically operate asynchronously and are often associated with the reset domain.
Clock and Reset Signals: Chisel modules often include input ports for clock and reset signals, allowing the module to be synchronized and reset externally.
Clock and Reset Methods: Chisel provides built-in methods for working with clock and reset signals, such as risingEdge and fallingEdge methods for detecting clock edges, and reset and resetTo methods for handling reset signals.
Crossing Clock Domains: In complex designs, it may be necessary to interface with multiple clock domains. Chisel provides mechanisms for handling clock domain crossings, including synchronizers and FIFOs.
Reset Configurations: Chisel allows for flexible configurations of reset signals, including active-high or active-low resets, synchronous or asynchronous resets, and different reset release mechanisms.

## Slide 16: 4. src/main/scala

## Slide 17: 4.1 Features of Scala
Conciseness: Scala is known for its conciseness and expressive syntax. It allows developers to write code with fewer lines and reduced boilerplate compared to Java.
Functional Programming: Scala supports functional programming paradigms, offering features such as higher-order functions, immutability, pattern matching, and support for lambda expressions. Java started incorporating functional programming features in later versions, but Scala has a stronger focus on functional programming from the beginning.
Type Inference: Scala has a powerful type inference system that can automatically deduce the types of variables and expressions. This reduces the need for explicit type declarations, making the code more concise and readable.
Immutable by Default: In Scala, variables are immutable by default, meaning they cannot be reassigned after initialization. This helps in writing safer and more thread-safe code. In Java, variables are mutable by default, but Java has introduced the final keyword to achieve immutability.
Traits: Scala provides traits, which are similar to interfaces but can also contain concrete method implementations. Traits allow for code reuse and composition, providing an alternative to single-inheritance interfaces in Java.
Pattern Matching: Scala has a powerful pattern matching mechanism that allows developers to match and destructure complex data structures. While Java has limited support for pattern matching in later versions, Scala's pattern matching capabilities are more comprehensive.

## Slide 18: 4.2 Classes
In Scala, classes serve as blueprints for creating objects. They can contain methods, values, variables, types, objects, traits, and other classes.
If you define a class parameter with var, it becomes a mutable field that can be reassigned. The parameter is visible outside the class, and you can access and modify its value directly.
If you define a class parameter with val, it becomes an immutable field that cannot be reassigned. The parameter is visible outside the class, and you can access its value directly, but you cannot modify it.
If you don't specify var or val for a class parameter, it becomes a private field that is only visible within the class. The parameter is not accessible outside the class, and you need to define getter and/or setter methods to access or modify its value.
class MyClass[Type1, Type2](parameter1: Type1, parameter2: Type2) {
  // Field 1: Description of field 1
  val field1: Type1 = ???
  // Field 2: Description of field 2
  var field2: Type2 = ???
  // Method 1: Description of method 1
  def method1(): Int = 3
  def method2(a: Int, b: Int): Int = {
    val c = a + b
    c - 9
  }
  // ...
}

## Slide 19: 4.3 Objects
In Scala, an object is a singleton instance of a class. It is a way to define a class and create an instance of that class at the same time.
Objects in Scala are similar to static classes in other languages, as they can contain methods, fields, and other members that can be accessed without creating an instance of the class.
Objects are defined using the object keyword followed by the name of the object.
class Person(val name: String)
object Employee extends Person("John") {
  def work(): Unit = {
    println(s"$name is working.")
  }
}
Employee.work()

## Slide 20: 4.4 Pattern matching
Pattern matching is a powerful feature in Scala that allows you to match and destruct the data structures based on their shape.
It provides a concise and expressive way to handle different cases and execute specific code based on the matched pattern.
A regular class needs an unapply method in a companion object of the class, which can decompose the object into its components and return them as a tuple. This allows the class to be used in pattern matching expressions, but case classes and objects make it easy.
If you want to avoid default case, seal the trait with keyword “sealed”.
def matchNumber(number: Int): String = number match {
  case 0 => "Zero"
  case 1 => "One"
  case 2 => "Two"
  case _ => "Other"
}
trait Vehicle
class Qingqi(val khokha: String, val engine: String)
object Qingqi {
  def unapply(vehicle: Qingqi): Option[(String, String)] = {
    Some((vehicle.khokha, vehicle.engine))
  }
}
case class Car(brand: String, model: String) extends Vehicle
case class Bike(brand: String, gears: Int) extends Vehicle
case object Train extends Vehicle
def displayVehicleInfo(vehicle: Vehicle): Unit = vehicle match {
  case Car(brand, model) => println(s"Car: $brand $model")
  case Bike(brand, gears) => println(s"Bike: $brand, Gears: $gears")
  case Train => println("Train")
  case Qingqi(khokha, engine) => println(s”khokha: $khokha, engine: $engine")
  case _ => println(”Vehicle")
}

## Slide 21: 4.5 Cake Pattern
The Cake Pattern is a design pattern used in Scala for achieving modularity and dependency injection.
It allows the composition of objects with different dependencies at compile time.
The pattern involves creating a set of traits, each representing a module or component of the application.
Each trait defines its dependencies as abstract members.
Concrete implementations of the traits provide the actual implementations of the dependencies.
Dependencies are wired together by mixing in the required traits into an object or class.
The pattern promotes loose coupling, as the dependencies are defined through abstract members rather than concrete types.
It enables easy swapping of dependencies by simply mixing in different implementations of the traits.
The pattern provides a flexible and modular way to structure applications and manage dependencies.
class BaseClass {
  def baseMethod(): Unit = {
    println("Base method")
  }
}
trait ExtendedTrait1 extends ExtendedClass{
  def extendedMethod(): Unit = {
    baseMethod()
    println("Extended method")
  }
}
trait ExtendedTrait2 { self: BaseClass =>
  def extendedMethod(): Unit = {
    baseMethod()
    println("Extended method")
  }
}
class ExtendedClass extends BaseClass with ExtendedTrait1
val obj = new ExtendedClass()
obj.extendedMethod()

## Slide 22: 4-6 Funtional programming
Immutable Data: Scala encourages the use of immutable data structures, which helps in writing pure functions and prevents unintended side effects.
First-Class Functions: Functions in Scala are treated as first-class citizens, meaning they can be assigned to variables, passed as arguments, and returned as results.
Higher-Order Functions: Scala supports higher-order functions, which means functions can take other functions as parameters or return functions as results.
Pure Functions: Pure functions in Scala have no side effects and always produce the same output given the same input, making them easier to reason about and test.
Function Composition: Scala provides convenient syntax for composing functions, allowing you to build complex computations by chaining together simpler functions.
Collections and Higher-Order Methods: Scala's collections library provides a rich set of higher-order methods like map, filter, and reduce, allowing for expressive and efficient data transformations.
// Higher-order function
def multiplyByTwo(x: Int): Int = x * 2
// Function composition using `andThen`
val addOneAndMultiplyByTwo: Int => Int = (x => x + 1) andThen multiplyByTwo
val result = addOneAndMultiplyByTwo(3)
// Output: 8
// Immutable data structure
val numbers: List[Int] = List(1, 2, 3, 4, 5)
// Pattern matching on a List
val filteredNumbers: List[Int] = numbers match {
  case head :: tail => tail // Remove the first element
  case _ => Nil // Return an empty list
}
// Recursive function to calculate the factorial of a number
def factorial(n: Int): Int = {
  if (n <= 1) 1
  else n * factorial(n - 1)
}
// Using map to transform a list of numbers
val numbers: List[Int] = List(1, 2, 3, 4, 5)
// Using `map` to transform each number in the list
val squaredNumbers: List[Int] = numbers.map(x => x * x)
println(squaredNumbers)
// Output: List(1, 4, 9, 16, 25)
// Using reduce to calculate the sum of a list of numbers
val numbers: List[Int] = List(1, 2, 3, 4, 5)
// Using `reduce` to calculate the sum of the numbers
val sum: Int = numbers.reduce((x, y) => x + y)
println(sum)
// Output: 15

## Slide 23: 5. Case Studies and Examples

## Slide 24: Recursive multiplier
https://github.com/tamood/recursive-multiplier

## Slide 25: 6. Resources and Further Reading

## Slide 26: 6.1 Recommended Books
https://github.com/schoeberl/chisel-book